## Slide 1: IT Essentials Common Problems and Solutions

## Slide 2
Components and Peripherals

## Slide 3
Problem
When booting a system to Windows, an “OS not found” error message is displayed when the computer is started.

## Slide 4
Probable Causes
The hard drive has failed.
The hard drive is not jumpered correctly.
The boot order is not set correctly in BIOS.
The MBR is corrupted.

## Slide 5
Possible Solutions
The hard drive has failed.
Replace the hard drive.

## Slide 6
Possible Solutions
The hard drive is not jumpered correctly.
Change the jumper settings on the hard drive (Master, Slave, or Cable Select).

## Slide 7
Possible Solutions
The hard drive has failed.
Replace the hard drive.

## Slide 8
Possible Solutions
The boot order is not set correctly in BIOS.
Change the boot order in BIOS to boot the correct hard drive.

## Slide 9
Possible Solutions
The MBR is corrupted.
Boot the computer to the Recovery Console. At the command prompt, use the bootrec /fixmbr or bootrec /fixboot in Windows 7 or Vista, or use the fixmbr command in Windows XP.

## Slide 10
Problem
When booting a computer with a RAID configuration, an error states, “RAID cannot be found.”

## Slide 11
Probable Causes
Cables connected to the hard drives are connected incorrectly.
The external RAID controller is not receiving power.
The RAID controller has failed.
The BIOS settings are incorrect.

## Slide 12
Possible Solutions
Cables connected to the hard drives are connected incorrectly.
Examine all of the cable connections to all of the drives in the array.

## Slide 13
Possible Solutions
The external RAID controller is not receiving power.
Check the power connection to the RAID controller.

## Slide 14
Possible Solutions
The RAID controller has failed.
Replace the RAID controller

## Slide 15
Possible Solutions
The BIOS settings are incorrect.
Reconfigure the BIOS settings for the RAID controller.

## Slide 16
Problem
RAID stops working.

## Slide 17
Probable Causes
The external RAID controller is not receiving power.
The RAID controller has failed.
The BIOS settings are incorrect.

## Slide 18
Possible Solutions
The external RAID controller is not receiving power.
Check the power connection to the RAID controller.

## Slide 19
Possible Solutions
The RAID controller has failed.
Replace the RAID controller.

## Slide 20
Possible Solutions
The BIOS settings are incorrect.
Reconfigure the BIOS settings for the RAID controller.

## Slide 21
Problem
A computer exhibits slow performance.

## Slide 22
Probable Causes
The computer does not have enough RAM.
The computer is running too many programs.
The hard drive is full.

## Slide 23
Possible Solutions
The computer does not have enough RAM.
Install additional RAM.

## Slide 24
Possible Solutions
The computer is running too many programs.
Close unneeded programs.

## Slide 25
Possible Solutions
The hard drive is full.
Run Disk Cleanup or replace the hard drive with a larger capacity drive.

## Slide 26
Problem
The computer does not recognize a SCSI drive.

## Slide 27
Probable Causes
The SCSI drive has an incorrect SCSI ID.
The SCSI termination is not set correctly.
The external SCSI drive was not powered on prior to booting the computer.

## Slide 28
Possible Solutions
The SCSI drive has an incorrect SCSI ID.
Reconfigure the SCSI ID.

## Slide 29
Possible Solutions
The SCSI termination is not set correctly.
Ensure that the SCSI chain is terminated at the correct end points.

## Slide 30
Possible Solutions
The external SCSI drive was not powered on prior to booting the computer.
Turn on the drive before booting the computer.

## Slide 31
Problem
A user calls and states that their new removable flash dice is not recognized by their computer when they plug it into their USB port.

## Slide 32
Probable Causes
The OS does not have the correct drivers for the removable external drive.
The USB port has too many attached devices to supply adequate power.

## Slide 33
Possible Solutions
The OS does not have the correct drivers for the removable external drive.
Download the correct drivers for the drive.

## Slide 34
Possible Solutions
The USB port has too many attached devices to supply adequate power.
Attach external power to the device or remove some of the USB devices.

## Slide 35
Problem
After updating the CMOS firmware, the computer will not start.

## Slide 36
Probable Causes
The CMOS firmware update did not install correctly.

## Slide 37
Possible Solutions
The CMOS firmware update did not install correctly.
Restore the original firmware from the onboard backup if there is one available
Contact the motherboard manufacturer to obtain a new CMOS chip.
If the motherboard has two CMOS chips, the second CMOS chip can be used.

## Slide 38
Problem
The computer reboots without warning, locks up, or displays error messages or the BSOD.

## Slide 39
Probable Causes
The front-side bus is set too high.
The CPU multiplier is set too high.
The CPU voltage is set too high.

## Slide 40
Possible Solutions
The front-side bus is set too high.
Reset the factory settings for the motherboard.
Lower the FSB setting.

## Slide 41
Possible Solutions
The CPU multiplier is set too high.
Reset the factory settings for the motherboard.
Lower the multiplier settings.

## Slide 42
Possible Solutions
The CPU voltage is set too high.
Reset the factory settings for the motherboard.
Lower the CPU voltage settings.

## Slide 43
Problem
After upgrading from a single core CPU to a dual core CPU, the computer runs slower and only shows one CPU graph in Task Manager.

## Slide 44
Probable Causes
The BIOS does not recognize the multi-core CPU.

## Slide 45
Possible Solutions
The BIOS does not recognize the multi-core CPU.
Update the CMOS firmware to support the multi-core CPU.