## Slide 1: IT Essentials Common Problems and Solutions

## Slide 2
Laptops

## Slide 3
Problem
The laptop screen appears black or very dim. A buzzing noise may also be heard.

## Slide 4
Probable Causes
Laptop display screen inverter or backlight lamp failure.

## Slide 5
Possible Solutions
Laptop display screen inverter or backlight lamp failure.
Replace the display inverter.
Replace the backlight lamp.

## Slide 6
Problem
The laptop screen only displays vertical lines that can change colors.

## Slide 7
Probable Causes
Laptop display screen failure.

## Slide 8
Possible Solutions
Laptop display screen failure.
Replace the laptop display screen.

## Slide 9
Problem
External laptop display connected to the laptop shows content but the laptop screen is blank.

## Slide 10
Probable Causes
The laptop screen is not set to display output.

## Slide 11
Possible Solutions
The laptop screen is not set to display output.
Press the Fn key with the appropriate multifunction key to display output on the laptop screen.

## Slide 12
Problem
Laptop display screen and external monitor will not display images, while the laptop hard drive and fans are operating normally.

## Slide 13
Probable Causes
The laptop motherboard or the video card has failed.

## Slide 14
Possible Solutions
The laptop motherboard or the video card has failed.
Replace the laptop motherboard if it has onboard video.
Replace the video card.

## Slide 15
Problem
The laptop does not return from Standby or Hibernate mode.

## Slide 16
Probable Causes
The laptop has a conflict between the BIOS settings and the Windows power management settings.

## Slide 17
Possible Solutions
The laptop has a conflict between the BIOS settings and the Windows power management settings.
Reconfigure the laptop BIOS settings and the Windows power management settings.

## Slide 18
Problem
The laptop hard drive has data access errors and makes unusual noises.

## Slide 19
Probable Causes
Hard drive has failed.

## Slide 20
Possible Solutions
Hard drive has failed.
Replace the hard drive.

## Slide 21
Problem
The laptop will not boot or access a newly installed hard drive.

## Slide 22
Probable Causes
The hard drive is not connected properly.
The BIOS does not recognize the new hard drive.

## Slide 23
Possible Solutions
The hard drive is not connected properly.
Reconnect the hard drive.

## Slide 24
Possible Solutions
The BIOS does not recognize the new hard drive.
Update the laptop BIOS.

## Slide 25
Problem
The laptop accesses the hard drive excessively.

## Slide 26
Probable Causes
The virtual memory is set incorrectly.
Additional RAM is needed.
Free hard drive space is limited.

## Slide 27
Possible Solutions
The virtual memory is set incorrectly.
Change the virtual memory settings.

## Slide 28
Possible Solutions
Additional RAM is needed.
Install additional RAM.

## Slide 29
Possible Solutions
Free hard drive space is limited.
Delete or remove unneeded files and applications.

## Slide 30
Problem
The laptop makes a long beeping noise after installing new RAM.

## Slide 31
Probable Causes
The wrong type of RAM is installed.
The RAM is installed incorrectly.
A damaged RAM module is installed.

## Slide 32
Possible Solutions
The wrong type of RAM is installed.
Install the correct type of RAM.

## Slide 33
Possible Solutions
The RAM is installed incorrectly.
Remove and reinstall the RAM.

## Slide 34
Possible Solutions
A damaged RAM module is installed.
Replace the damaged RAM module.

## Slide 35
Problem
The laptop LED power light is not on when the laptop is plugged into an AC outlet.

## Slide 36
Probable Causes
The AC power source is not working.
The power cable is not securely connected to the laptop.
The AC adapter is defective.

## Slide 37
Possible Solutions
The AC power source is not working.
Plug the laptop into a known good power source.

## Slide 38
Possible Solutions
The power cable is not securely connected to the laptop.
Unplug and securely connected the power cable to the laptop.

## Slide 39
Possible Solutions
The AC adapter is defective.
Replace the AC adapter.